## Slide 1: Lecture 2 Computer Communications and Networks
Boriana Koleva
Room: C56
Phone: 84 66530
Email: B.Koleva@nottingham.ac.uk

## Slide 2: Introduction
Local communication
  Encoding data
  LANs
Long Distance communication
  Modulation
  Modems and broadband connections

## Slide 3: Transmission Media
Copper Wires
  Twisted Pair
  Coaxial
Fibre Optic
Radio
Microwave
Infrared
Satellites

## Slide 4: Transmitting data over short distance
Changes in electric current used to transmit bits over short distance
  E.g. RS-232 (serial port)
Voltage
+
-
1 0 1 0 0 0
Time

## Slide 5: Shared Communication Channels
Early local networks used dedicated links between each pair of computers
  But poor scalability
Shared LANs invented in the 1960s
Rely on computers sharing a single medium
Computers coordinate their access
Low cost
But not suitable for wide area - communication delays inhibit coordination

## Slide 6: Local Area Network (LAN)
How are computers wired together in a LAN? – 3 common topologies
hub
Star
Ring
Bus (shared cable)

## Slide 7: Ethernet
Ethernet is a bus LAN topology
Invented at Xerox PARC in the early ’70s
Developed commercially by 3COM later
Standards controlled by IEEE
Today it is the most widely used network topology for LANs

## Slide 8: Older Ethernet wiring schemes
“Thick” Ethernet
  The original Ethernet standard
  Coaxial cable – computers connected via transceivers
“Thin” Ethernet
  Coaxial cable – computers directly connected via BNC

## Slide 9: Twisted Pair Ethernet
Is twisted pair Ethernet a bus or star?
  Logically it is a bus
  Physically it is a star

## Slide 10: Sharing the Ether
Data is divided into small chunks called “packets” which may be one of a number of standard types
A packet sent from one computer propagates to either end of the cable
The packet is ignored by every computer on the network except the destination computer

## Slide 11: Ethernet Co-ordination
Ethernet systems do not have a central controller telling computers when they can talk
All computers on an Ethernet network use Carrier Sense Multiple Access (CSMA)
  The electrical activity that occurs during packet transmission is called the carrier
  Before transmitting a packet a computer checks for a carrier and only transmits when the network is quiet
  Checking for a carrier is called Carrier Sense
  The whole process is CSMA

## Slide 12: Collision Detection
CSMA prevents computers from interrupting ongoing transmissions
CSMA does not prevent simultaneous transmissions
Simultaneous signals will interfere – this is called a collision, which will damage data in both packets
Ethernet has collision detection (CD)
  The sending computer monitors the signal on the ether
  If this signal differs from what was sent a collision must have occurred
The whole system is CSMA/CD

## Slide 13: Collision Handling
When CSMA/CD detects a collision, both computers must re-send their data
This does not happed immediately (to avoid another collision)
Both computers wait a random amount of time (the maximum allowed is a part of the Ethernet standard)
The data is sent again, once the network is quite
If there is a second, collision the maximum delay is doubled, etc.
Exponential backoff

## Slide 14: Sending bits over long distance
Encoding data as discrete voltage changes does nt work over long distance as the signal attenuates
A continually oscillating wave travels further
Bits of data are modulated onto a carrier wave
Modulation and demodulation is done by a modem

## Slide 15: Amplitude Modulation

## Slide 16: Frequency Modulation

## Slide 17: Phase shift modulation

## Slide 18: Modems
Hardware that takes bits and applies modulation is a modulator
Hardware that takes a modulated wave and extracts bits is a demodulator
Full duplex communication requires a combined modulator-demodulator (MODEM) at both ends

## Slide 19: Example modem connection

## Slide 20: Dial-up modem configuration

## Slide 21: Terminology
Bandwidth – the number of signals per second that a medium can accommodate
Multiplexing - several logical connections share a single physical connection
Broadband - a transmission method which supports a relatively wide range of frequencies which may be divided into channels

## Slide 22: Digital Subscriber Line (DSL)
Uses the two-wire local loop from the local telephone exchange to homes
Normal telephone lines are limited to the frequency range of human voices (0-3400 Hz)
DSL uses the entire bandwidth of the local loop
However, capacity decreases with connection distance
  limit 18,000 feet (5,460 m)
Telephone exchange

## Slide 23: Digital Subscriber Line (DSL)
DMT (Discrete MultiTone) divides the data into 247 separate channels, each 4 KHz wide
  equivalent of 247 modems connected to your computer at once!
  Channel 0 is used for voice
  Usually 80-90% of the rest of the channels are used for downstream communication (Asymmetrical DSL)

## Slide 24: Digital Subscriber Line (DSL)
ADSL speed – max. downstream 8 Mbps and max. upstream 1 Mbps
  up to distance of 2 km
ADSL2+ can deliver up to 24 Mbps (downstream)

## Slide 25: Cable Connection
Cable television
Fixed telephone system
- A single cable is shared by many houses
+ Bandwidth of coax much higher than TP

## Slide 26: Cable Connection
Sharing the cable for Internet and TV
To cope with long coaxial cables analog modulation is needed
A cable modem connect a computer (through USB or Ethernet interface) to the cable network

## Slide 27: Summary
Local communication
  Encoding data
  LANs
    Topologies
    Ethernet (wiring schemes and coordination)
Long Distance communication
  Modulation
  Modems and broadband connections